## Slide 1: Moisil’s simplification method for Boolean functions
Crîșmariu Ioana-Teodora
Group 912

## Slide 2: Problem statement
8.Using Moisil’s method simplify the following Boolean function of three variables:
f8 (x1, x2 , x3) = m0 v m3 v m4 v m6 v m7

## Slide 3: Theoretical result
Simplifying a Boolean function (given in disjunctive canonical form) means covering all its minterms with a minimum number of maximal monoms and a minimum number of overlaps
Simplification process steps ( steps 2, 3 are specific to Moisil’s method, which is an algebraic simplification method) :
The initial function f is transformed into DCF(f).
The set of maximal monoms are calculated using either one of Veitch-Karnaugh diagrams ( a graphical method) or Quine’s method ( an analytical method). For simplifying f8 we will use Quine’s method.
In order to obtain the simplified forms of the function from the set of maximal monoms, we will use propositional logic.

## Slide 4: Quine’s method
Since our initial function (f8 (x1, x2, x3) = m0 v m3 v m4 v m6 v m7 = v v v v ) is already given in DCF, we will jump straight to the factorization process. We will use Quine’s method in order to find the set of maximal monoms M(f).
Sf = {(0, 0, 0), (0, 1, 1), (1, 0, 0), (1, 1, 0), (1, 1, 1)} – the support set of f
The first step of Quine’s method is to order the support set of f with respect to the number of “1” values in each 3-tuple.
Sf = {(0, 0, 0), (1, 0, 0), (1, 1, 0), (0, 1, 1), (1, 1, 1)} (ascending order)
The minterms from the function’s expression are represented using the powers of variables, in a tableau, each minterm on a line, in ascending/ descending order, with respect to the number of “1” values in the 3-tuples of the support of the function. The header of the tableau contains the variables’ names.

## Slide 5: Sf = {(0, 0, 0), (1, 0, 0), (1, 1, 0), (0, 1, 1), (1, 1, 1)}
x1 | x2 | x3
0 | 0 | 0
1 | 0 | 0
1 | 1 | 0
0 | 1 | 1
1 | 1 | 1
- | 0 | 0
1 | - | 0
1 | 1 | -
- | 1 | 1
I
II
III
IV
V = I + II
VI = II + III
VII = III + IV
m0
m4
m6
m3
m7
m0 v m4 = = max1
☺
☺
m4 v m6 = = max2
☺
m6 v m7 = = max3
m3 v m7 = = max4
☺
☺
The result of the factorization of the neighbor monoms from the neighbor groups is a new monom represented as a row at the end of the tableau. The row contains the same values in the columns corresponding to the common variables of the adjacent monoms and the symbol ”-” for the variable which is eliminated. The rows corresponding to the neighboring monoms used are marked on the left side, meaning they are not maximal monoms.

## Slide 6
The set of maximal monoms obtained:
M(f) = { , , , } = {max1, max2, max3, max4}
Because the simplified forms of a function contain only maximal monoms we consider the following propositional sentences:
pi : “ maxi belongs to the simplified form of f ”, i = 1,2,..,4

## Slide 7
Overview of the factorization process: four simple factorizations were applied.
max1 = m0 v m4 = max2 = m4 v m6 =
max3 = m6 v m7 = max4 = m3 v m7 =
Each minterm from the function’s expression must be covered by a maximal monom in a simplified form, therefore according to the result of the factorization process we have the following true sentences:
“m0 is covered by max1”, translated as p1 ≡ T
“m4 is covered by max1 or by max2’’, translated as p1 v p2 ≡ T
“m6 is covered by max2 or by max3”, translated as p2 v p3 ≡ T
“m3 is covered by max4”, translated as p4 ≡ T
“m7 is covered by max3 or by max4”, translated as p3 v p4 ≡ T

## Slide 8
All the minterms from the function’s expression must be covered by a minimum number of maximal monoms, with a minimum number of overlaps. This statement is modelled by the following propositional formula obtained as a conjuction of al previous true sentences:
p1 ˄ (p1 v p2) ˄ (p2 v p3) ˄ p4 ˄ (p3 v p4) ≡ T (CNF with 5 clauses)
This CNF is then transformed into a DNF.
Through repeated use of distributive laws, we get to:
T ≡ (p1 ˄ p1 ˄ p2 ˄ p4) v (p1 ˄ p2 ˄ p2 ˄ p4) v (p1 ˄ p1 ˄ p3 ˄ p4) v (p1 ˄ p2 ˄ p3 ˄ p4)
Apply idempotency:
T ≡ (p1 ˄ p2 ˄ p4) v (p1 ˄ p2 ˄ p4) v (p1 ˄ p3 ˄ p4) v (p1 ˄ p2 ˄ p3 ˄ p4)
Apply absorbtion laws:
T ≡ (p1 ˄ p2 ˄ p4) v (p1 ˄ p3 ˄ p4) (DNF with 2 cubes is obtained)

## Slide 9
T ≡ (p1 ˄ p2 ˄ p4) v (p1 ˄ p3 ˄ p4) (DNF with 2 cubes)
A DNF (disjunction of cubes) is true is at least one of its cubes is true.
From DNF we consider the cubes with the minimum number of propositional variables and correspondingly we obtain the simplified forms of f.
For the cube (p1 ˄ p2 ˄ p4) ≡ T the corresponding simplified form is:
(x1, x2, x3) = max1 v max2 v max4 = v v
For the cube (p1 ˄ p3 ˄ p4) ≡ T the corresponding simplified form is:
(x1, x2, x3) = max1 v max3 v max4 = v v