## Slide 1: Individual Homework
Cotor Catinca, group 912

## Slide 2: Exercise 4.2 Boolean Functions
Simplify the following Boolean functions of 4 variables using Veitch diagrams.

## Slide 3: Theoretical results
Simplification of boolean functions
Informally, to simply a Boolean function given in disjunctive canonical form, means to cover all its minterms with a minimum number of maximul monoms and with a minimum number of overlaps.
The simplification process is formalized by the steps below:
The initial function f is transformed into DCF(f).
Factorization process => the set of maximal monoms M(f).
From the set of maximal monoms the central monoms are selected => C(f).
The case of the simplification algorithm is identified and all simplified forms are obtained.

## Slide 4: Simplification algorithm

## Slide 5: Theoretical results
Veitch-Karnaugh Diagrams Method
The cells in a Veitch diagram are arranged so that there is only a single variable change.
Adjancy(graphical neighborhood) relation is defined by a single variable change.
The diagrams are circular, meaning that the first row/column and the last row/column are neighbors.
Two minterms belonging to two neighbor cells factorize => simple factorization.
The result of k-factorization is a monom which contains the column variables of all 2k neighbor minterms.
The maximal monoms are obtained from the diagram by applying factorization as follows: for a Boolean function of n variables we try first: n-factorization, we continue with n-1 factorization, …,
simple factorization and 0-factorization(isolated minterms).

## Slide 6: Theoretical results
Veitch-Karnaugh Diagrams Method
Factorization process => the set of maximal monoms M(f).
From the set of maximal monoms the central monoms are seleted => C(f).
The central monoms are the maximal monoms which cannot be coverred by the disjunction of all the other maximal monoms.
Identification of the central monoms:
  If the group of the minterms coverred by a maximal monom contains at least one cell circled once, then the maximul monom is a central and it belongs to all the simplified forms of the function.
The groups of the minterms corresponding to the central monoms are shaded in the diagram.
The minterms from the function's expression which are unshaded, are not coverred by the central monoms and they will be coverred in all the possible ways using a minimum number of unused maximal monoms and with a minimum number of overlaps, resulting all the simplified forms of the initial function.

## Slide 7: Problem solution
f(x1, x2,x3,x4) = x1x2 ∨ x1x̄2x̄3x4 ∨ x̄1x̄2x4∨ x̄1x3∨ x2x3 =
= x1x2x3x4 ∨ x1x2x̄3x̄4 ∨ x1x2x3x̄4 ∨ x1x2x̄3x4 ∨ x1x̄2x̄3x4 ∨ x̄1x̄2x3x4 ∨ x̄1x̄2x̄3x4 ∨ x̄1x2x3x4 ∨ x̄1x̄2x3x̄4∨ x̄1x2x3x̄4 =
= m15 ∨ m12 ∨ m14 ∨ m13 ∨ m9 ∨ m3 ∨ m1 ∨ m7 ∨ m2 ∨ m6
Click to add text
m15 | m13 |  | m7
m14 | m12 |  | m6
 |  |  | m2
 | m9 | m1 | m3
x̄1
x̄2
x̄3
x̄4
x2​
x1​
x3
x3​
x4
x4
Veitch Diagram
Factorization process
m15​ | m13​ | ​ | m7​
m14​ | m12​ | ​ | m6​
​ | ​ | ​ | m2​
​ | m9​ | m1​ | m3​
x̄3
x3
x3​
x̄2
x2​
x̄1
x1​
x̄4
x4
x4
- 3 groups of 4 neighboor minterms
- 2 groups of 2 neighboor minterms

## Slide 8: Factorization process Double factorization
Maximal monom: max1 = x1x2
Maximal monom: max2 = x̄1x3
m15​ | m13​ | ​ | m7​
m14​ | m12​ | ​ | m6​
​ | ​ | ​ | m2​
​ | m9​ | m1​ | m3​
x̄1
x1​
x̄2
x2​
x̄4
x4
x4
x̄3
x3
x3​
m15​ | m13​ | ​ | m7​
m14​ | m12​ | ​ | m6​
​ | ​ | ​ | m2​
​ | m9​ | m1​ | m3​
x̄1
x1​
x̄2
x2​
x̄4
x4
x4
x̄3
x3
x3​
m15​ | m13​ | ​ | m7​
m14​ | m12​ | ​ | m6​
​ | ​ | ​ | m2​
​ | m9​ | m1​ | m3​
x̄1
x1​
x̄2
x2​
x̄4
x4
x4
x̄3
x3
x3​
Maximal monom: max3 = x2x3

## Slide 9: Factorization process Simple factorization
Maximal monom: max4 = x̄2x̄3x4
Maximal monom: max5 = x̄1x̄2x4
m15​ | m13​ | ​ | m7​
m14​ | m12​ | ​ | m6​
​ | ​ | ​ | m2​
​ | m9​ | m1​ | m3​
x̄1
x1​
x̄2
x2​
x̄4
x4
x4
x̄3
x3
x3​
m15​ | m13​ | ​ | m7​
m14​ | m12​ | ​ | m6​
​ | ​ | ​ | m2​
​ | m9​ | m1​ | m3​
x̄1
x1​
x̄2
x2​
x̄4
x4
x4
x̄3
x3
x3​
The set of maximal monoms:
M(f) = {max1, max2, max3, max4, max5} =
= {x1x2 , x̄1x3 , x2x3 , x̄2x̄3x4 , x̄1x̄2x4 }.

## Slide 10: Central monoms
A maximal monom is a central monom if its correesponding group of minterms contains at least one minterm circled once.
C(f) = {max1, max2, max4} = {x1x2 , x̄1x3 , x̄2x̄3x4}
The minterms coverred by the central monoms are shaded.
M(f) ≠ C(f) and C(f) ≠ ∅ -- the second case of simplification.
We denote g = max1 V max2 V max4 = x1x2 V x̄1x3 V x̄2x̄3x4
The minterms covvered by g are shaded in the diagram and no minterm left uncoverred so there is just one simplification:
f S(x1x2x3x4) = max1 V max2 V max4 = x1x2 V x̄1x3 V x̄2x̄3x4
m15​ | m13​ | ​ | m7​
m14​ | m12​ | ​ | m6​
​ | ​ | ​ | m2​
​ | m9​ | m1​ | m3​
x̄3
x3
x3​
x̄2
x2​
x̄1
x1​
x̄4
x4
x4