## Slide 1: Individual Homework
Boolean Functions
Exercise 6.2
Using Quine’s method, simplify the following Boolean functions given in DCF (disjunction of minterms):
f2(x1, x2, x3) = m1 ∨ m2 ∨ m4 ∨ m5 ∨ m6 ∨ m7
Creț Valentina Andreea
Group 912

## Slide 2: THEORETICAL RESULTS
Quine’s method

## Slide 6
f2(x1, x2, x3) = m1 ∨ m2 ∨ m4 ∨ m5 ∨ m6 ∨ m7
= x10 x20 x31 ∨ x10 x21 x30 ∨ x11 x20 x30 ∨ x11 x20 x31 ∨ x11 x21 x30 ∨ x11 x21 x31
= x̅1 x̅2 x3 ∨ x̅1 x2 x̅3 ∨ x1 x̅2 x̅3 ∨ x1 x̅2 x3 ∨ x1 x2 x̅̅3 ∨ x1 x2 x3
Sf = {(0,0,1), (0,1,0), (1,0,0), (1,0,1) , (1,1,0) , (1,1,1)}
- Sorted in ascending order, with respect to the number of “1” values in each triple

## Slide 7
Group | x1 | x2 | x3 | Reprezentation / factorization
Ⅰ | 0 0 1 | 0 1 0 | 1 0 0 | m1 m2 m4
Ⅱ | 1 1 | 0 1 | 1 0 | m5 m6
Ⅲ | 1 | 1 | 1 | m7
Ⅳ = Ⅰ + Ⅱ
- 0 1
- 1 0
1 - 0
1 0 -
1 - 1
1 1 -
1 - -
m1 ∨ m5 = x̅2 x3
Simple factorization
Double factorization
m2 ∨ m6 = x2 x̅̅3
m4 ∨ m5 = x1 x̅̅2
m4 ∨ m6 = x1 x̅̅3
m5 ∨ m7 = x1 x3
m6 ∨ m7 = x1 x2
m4 ∨ m5 ∨ m6 ∨ m7 = x1
= max1
= max2
= max3
✓
✓
✓
✓
✓
✓
✓
✓
✓
✓
Ⅴ = Ⅱ + Ⅲ
Ⅵ = Ⅳ + Ⅴ

## Slide 8
M(f) = {max1, max2, max3}
Maximal monoms/ minterms | max1 | max2 | max3
m1 |  |  | 
m2 |  |  | 
m4 |  |  | 
m5 |  |  | 
m6 |  |  | 
m7 |  |  | 
max1 = m1 ∨ m5 = x̅2 x3
max2 = m2 ∨ m6 = x2 x̅̅3
max3 = m4 ∨ m5 ∨ m6 ∨ m7 = x1
*
*
*
*
*
*
*
*
Օ
Օ
Օ
C(f) = {max1, max2, max3}
M(f) = C(f) => 1st simplification case
There is a unique simplified form of f2, obtained as the disjunction of all central monoms.
f2s = max1 ∨ max2 ∨ max3 = x̅2 x3 ∨ x2 x̅̅3 ∨ x1
Օ

## Slide 9: Conclusion
The simplified form (using Quine’s method) of the Boolean function given is:
f2s = max1 ∨ max2 ∨ max3 = x̅2 x3 ∨ x2 x̅̅3 ∨ x1